## Slide 1
The target layout on the following slide is applicable to vehicles that meet the following criteria:
Front camera to front axle distance (A) between 850 mm and 1200 mm.
Total Vehicle Length (A+B) between 4650 mm and 6000 mm.
Total vehicle Width between 1800 mm and 2200 mm.
Centerline of front axle
A
B
C
Applicable Vehicle Dimensions for Assembly Plant Target Layout for 360 Degree Camera Alignment

## Slide 2
Assembly Plant Target Layout for 360 Degree Camera Alignment
5200 +/- 10
8200 +/- 10
1675
1850
+/- 5
Station
centerline
All dimensions are in millimeters (mm)
All targets and tires must be on a common plane. I.e. the entire station shall be flat (flat does not necessarily mean level)
The maximum height of the target above the flat plane on which the tires are sitting is 5.0 mm
The station layout must be “square”
Vehicle centerline must be within
+/- 500 mm lateral offset from station centerline and +/- 5.0 degrees of station centerline
Front axle centerline. Vehicle fore/aft stop tolerance is +/- 100mm
White squares are
500 mm x 500 mm +/- 5 mm and centered within black squares to within +/- 5 mm
Black target borders are
a minimum of 200 mm thick with a matte finish and a contrast of 1.4 or greater compared to inner white target square
1425
+/- 5
1425
+/- 5
1425
+/- 5
1425
+/- 5
Ambient Lighting must be greater than 150 Lux

## Slide 3
6630mm
minimum
1030 mm minimum
Adjacent Stations
Adjacent station must be at least 1030 mm apart, or they must share the center row of targets
(as shown on next slide), or vertical screening between stations is required.

## Slide 4
4700 mm
Shared center
row of targets
Adjacent Stations – Shared Center Row of Targets
This is an acceptable implementation of adjacent stations.

## Slide 5
Place a tire detent that will be sufficient for the operator to feel and to cradle front tire of wheel so that
The front axle is positioned within the +/- 100 mm tolerance as shown on slide 2, does not raise the
wheel by greater than 5mm when in cradle position and will also allow tire to completely drive over.
Controlling Stop Position

## Slide 6
a
Angle “a” cannot exceed 5 degrees which means:
Largest slot width “sw” = Minimum tire width “tw” + minimum wheelbase “wb” x Tan 5 degrees
sw = tw + wb x tan(5 degrees)
sw
tw
wb
Controlling the Yaw Angle
Car wash style guide rails.
Care should be taken to not damage wheels or tires

## Slide 7: 360 Surround View Alignment Process
MEC has to be unlocked.
Drive vehicle in amongst targets and position within specified tolerances
Place transmission in park.
Leave engine running.
Make sure outside rearview mirrors are folded out into detents for driving position.
Make sure all doors, hood, and trunk are closed completely.
Trigger onboard alignment process by turning parking light switch from “off” to "on" three times within a 10 second window of time. Also the alignment process can be triggered by serial data communication interaction as defined in the latest versions of the Active Safety Alignment Tester to ECU Interaction and Active Safety Alignment Status PID Definition specifications. (CPID $23)
Watch 360 view display in vehicle to see progress (see next 4 slides). Once triggered the process is less than 15 seconds.

## Slide 8
This display will be shown immediately after the learn process has been triggered, and will stay only for a very short duration (to the extent where it may not even be noticed, or appear to “flash” by).

## Slide 9
This display will be shown next and will indicate the images of the targets have been captured and are being processed within the electronic control unit. The processing of the images could take up to 7 seconds and this display will be shown the entire duration of the image processing.

## Slide 10
This display will be shown next and will indicate successful completion of the learn process and will remain for approximately 5 seconds before the display is returned to the normal mode. The vehicle can be moved from the station immediately upon display of this screen.

## Slide 11
This display could be shown instead of the green check and would indicate a failed learn attempt and will remain for approximately 5 seconds before the display is returned to the normal mode. The vehicle can be moved from the station immediately upon display of this screen, or the alignment process could be reattempted by going through the switch sequence indicated on slide 4, line item 6.
Vehicles that have not successfully completed the learn process will fail DVT.

## Slide 12
Normal mode of display after system has successfully learned
360 surround view portion of the display

## Slide 13
360 surround view portion of the display
Indicates 360 surround view system has never been successfully learned
Normal mode of display before system has successfully learned

## Slide 14
CPID to Tester Interaction

## Slide 15: Backup